STM32 PLC – OpenSourceLogger Protocol
# Introduction
STM32 PLC is the USB slave unit and OpenSourceLogger is the logging software.
# Protocol
## TX CAN Bus message OpenSourceLogger → STM32 PLC
Transmitted on GUI event:
Byte 0	Byte 1	Byte 2	to	Byte 5	Byte 6	Byte 7	to	Byte 15
Message type	IDE	ID MSB ID LSB			DLC	Data MSB Data LSB

Byte	Value	Comment
Message type	0x1	For STM32 PLC
IDE	0x0 or 0x4	0x0 = Standard ID, 0x4 = Extended ID
ID	0x0 to 0xFFFFFFFF	For both standard ID and extended ID
DLC	0x0 to 0x8	Length of data
Data	0x0 to 0xFF	Message data

Receive: No response back
## RX CAN Bus message STM32 PLC→ OpenSourceLogger
Transmitted when STM32 PLC got a CAN message:
Byte 0	Byte 1	Byte 2	to	Byte 5	Byte 6	Byte 7	to	Byte 15
Message type	IDE	ID MSB ID LSB			DLC	Data MSB Data LSB

Byte	Value	Comment
Message type	0x0	For OpenSourceLogger
IDE	0x0 or 0x4	0x0 = Standard ID, 0x4 = Extended ID
ID	0x0 to 0xFFFFFFFF	For both standard ID and extended ID
DLC	0x8	Length of data.
Data	0x0 to 0xFF	Message data

Receive: No response back
## Control message OpenSourceLogger → STM32 PLC
Transmitted every 1 millisecond:
Byte 0	Byte 1	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5
Message type	PWM0 MSB	PWM0 LSB	PWM1 MSB	PWM1 LSB	PWM2 MSB	PWM2 LSB

Byte 6	Byte 7	Byte 8	Byte 9	Byte 10	Byte 11
PWM3 MSB	PWM3 LSB	PWM4 MSB	PWM4 LSB	PWM5 MSB	PWM5 LSB

Byte 12	Byte 13	Byte 14	Byte 15	Byte 16	Byte 17
PWM6 MSB	PWM6 LSB	PWM7 MSB	PWM7 LSB	AO0 MSB	AO0 LSB

Byte 18	Byte 19	Byte 20	Byte 21
AO1 MSB	AO1 LSB	AO2 MSB	AO2 LSB

Byte	Value	Comment
Message type	0x3	For STM32 PLC
PWMx	0x0 to 0xFFFF	16-bit PWM control period
AOx	0x0 to 0xFFF	12-bit Analog output

Receive measurements back:
Byte 0	Byte 1	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5
Message type	DI0	DI1	DI2	DI3	DI4	DI5

Byte 6	Byte 7	Byte 8	Byte 9	Byte 10	Byte 11	Byte 12
DI6	DI7	DI8	ADC0 MSB	ADC0 LSB	ADC1 MSB	ADC1 LSB

Byte 13	Byte 14	Byte 15	Byte 16	Byte 17	Byte 18	Byte 19
ADC2 MSB	ADC2 LSB	ADC3 MSB	ADC3 LSB	ADC4 MSB	ADC4 LSB	ADC5 MSB

Byte 20	Byte 21	Byte 22	Byte 23	Byte 24	Byte 25	Byte 26
ADC5 LSB	ADC6 MSB	ADC6 LSB	ADC7 MSB	ADC7 LSB	ADC8 MSB	ADC8 LSB

Byte 27	Byte 28	Byte 29	Byte 30	Byte 31	Byte 32	Byte 33
ADC9 MSB	ADC9 LSB	ADC10 MSB	ADC10 LSB	ADC11 MSB	ADC11 LSB	DADC0 MSB

Byte 34	Byte 35	Byte 36	Byte 37	Byte 38	Byte 39	Byte 40
DADC0 LSB	DADC1 MSB	DADC1 LSB	DADC2 MSB	DADC2 LSB	DADC3 MSB	DADC3 LSB

Byte 41	Byte 42	Byte 43	Byte 44	Byte 45	Byte 46	Byte 47
DADC4 MSB	DADC4 LSB	ENCODER0 MSB	ENCODER0 LSB	ENCODER1 MSB	ENCODER1 LSB	IC0 MSB

Byte 48	Byte 49	Byte 50
IC0 LSB	IC1 MSB	IC1 LSB

Byte	Value	Comment
Message type	0x2	For OpenSourceLogger
ADCx	0x0 to 0xFFFF	16-bit ADC measurement
DADCx	0x0 to 0xFFFF	16-bit Differential ADC measurement
ENCODERx	0x0 to 0xFFFF	16-bit Encoder measurement
ICx	0x0 to 0xFFFF	16-bit Input Capture measurement

## PWM prescaler set OpenSourceLogger → STM32 PLC
Transmitted on GUI event:
Byte 0	Byte 1	Byte 1	Byte 2
Message type	Peripherial	Prescaler MSB	Prescaler LSB

Receive: No response back

Byte	Value	Comment
Message type	0x5	For STM32 PLC
Peripherial	0x0 or 0x1	0x0 = PWM 0 to 3, 0x1 = PWM 4 to 7
Prescaler	0x0 to 0xFFFF	16-bit PWM prescaler

## Sigma Delta ADC gain set OpenSourceLogger → STM32 PLC
Transmitted on GUI event:
Byte 0	Byte 1	Byte 1	Byte 2
Message type	SDADC	Configuration index	Gain

Receive: No response back

Byte	Value	Comment
Message type	0x4	For STM32 PLC
SDADC	0x1, 0x2 or 0x3	What type of Sigma Delta peripheral
Configuration index	0x0 to 0x2	Type of configuration index for Sigma Delta
Gain	0x0 to 0x7	Type of gain

## Sigma Delta ADC gains request OpenSourceLogger → STM32 PLC
Transmitted on GUI event:
Byte 0	Byte 1
Message type	SDADC

Byte	Value	Comment
Message type	0x7	For STM32 PLC
SDADC	0x1, 0x2 or 0x3	What type of Sigma Delta peripheral

Receive three gains:
Byte 0	Byte 1	Byte 2	Byte 3
Message type	Gain 0	Gain 1	Gain 2

Byte	Value	Comment
Message type	0x7	For OpenSourceLogger
Gain 0	0x0 to 0x7	Gain for configuration index 0
Gain 1	0x0 to 0x7	Gain for configuration index 1
Gain 2	0x0 to 0x7	Gain for configuration index 2

## PWM prescalers request OpenSourceLogger → STM32 PLC
Transmitted on GUI event:
Byte 0
Message type

Byte	Value	Comment
Message type	0x6	For STM32 PLC

Receive two prescalers:
Byte 0	Byte 1	Byte 2
Message type	Prescaler 0	Prescaler 1

Byte	Value	Comment
Message type	0x6	For OpenSourceLogger
Prescaler 0	0x0 to 0xFFFF	Prescaler for PWM 0 to PWM 3
Gain 1	0x0 to 0xFFFF	Prescaler for PWM 4 to PWM 7